## Slide 2: Cu Metals Marina Study – Lower Newport Bay OC Coastkeeper (Ray Hiemstra) Santa Ana RWQCB (Linda Candelaria, PhD) City of Newport Beach

## Slide 3: Lower Newport Bay Copper/ Marinas Metals Study

## Slide 4: Objectives
Determine whether Cu antifouling boat paints are a significant source of Cu to the water & sediments in marinas and Lower Newport Bay
Determine metal concentrations in water and sediment in marinas and adjacent channel sites
Determine toxicity in marinas & channels

## Slide 5: Methodology -sampling
Collect water and sediment samples throughout Lower Newport Bay
Sites – 8 marinas & adjacent channels
(3 stations/marina, 1 station in channel)
+ 2 storm drain sites, 1 shipyard site
3 sampling events: May, August, December
1 supplemental sampling: November
-August –Toxicity analyses on subset of 10 samples

## Slide 6: Methodology cont.
Chemical Analysis
Water – dissolved & total metals, TSS, DOC, salinity
Sediment – metals
Aug -additional -(10 samples) -PCBs, PAHs, toxicity (water & sed) , sediment TOC, PSA, AVS/SEM
Toxicity Analysis (10 samples)
-Water – mussel embryo,
-Sediment – amphipod (Eohaustorius),
–sediment/water interface, pore water

## Slide 7: Results
Water –
Only Dissolved Cu above CTR standards
(tested Cu, Cd, Cr, Zn, As, Hg, Pb, Ni )
Mean dissolved Cu concentrations mostly above mean channel concentrations

## Slide 9: Results
Sediment –
Sediment Cu, Hg, Zn above ERMs
Marina means mostly higher than channel means

## Slide 17: Dissolved Metals
 | Marina mean (ug/L) | Channel mean (ug/L)
Cu | 4.26* *>CTR chronic (3.1) | 3.11* *>CTR chronic (3.1)
Zn | 18.61 | 15.21
Cd | 0.07 | 0.05
Pb | 0.02 | 0.01
As | 1.11 | 1.13
Hg | Nd | Nd

## Slide 18: Sediment Metals
 | Marina mean (ug/g) | Channel mean (ug/g) | **exceeds ERL
Cu | 184.81** | 106.2** | 34 (ug/g)
Zn | 288.43** | 197.43** | 150
Hg | 0.55** | 0.35** | 0.15
Cd | 1.32** | 1.08 | 1.2
Pb | 36.77 | 31.28 | 46.7
As | 9.72** | 7.51 | 8.2

## Slide 19: Objectives
Determine whether Cu antifouling boat paints are a significant source of Cu to the water & sediments in marinas and Lower Newport Bay
Determine metal concentrations in water and sediment in marinas and adjacent channel sites
Test for toxicity in marinas & channels

## Slide 20: Conclusions
Water
Dissolved Copper only metal above CTR standards
acute & chronic (4.8, 3.1 ug/L)
(biggest source of Cu is boat paints ~ 60,000 lbs/yr )
Most dissolved Cu marina means & half channel means above CTR
Mean dissolved Cu concentrations mostly above mean channel concentrations (altho not statistically significant)
Highest dissolved Cu concentrations in W Newport
No Water Toxicity Found

## Slide 21: Conclusions cont.
Sediment
Sediment Cu, Hg, Zn above ERMs,
Sediment Cu, As, Cd, Cr, Hg, Pb and Zn above ERLs
Marina means mostly higher than channel means (statistically significant in 5/8marinas)
-highest sediment concentrations in W Newport, lowest in Dunes, DeAnza

## Slide 22: Conclusions cont.
Sediment Toxicity
Sediment toxicity found at 8/10 stations tested (6/8 marinas) w/Eohaustorius
Pore water tests showed reduced %alive altho results were inconclusive
Data suggests that Cu boat paints are significant source of Cu to marina waters and sediments